## Slide 1: Portable User Interface For Cyber Security Awareness
By: Nicholas Jones

## Slide 2: Most creations Arise from problem solving
iPhone
Steam Engine
Wheel

## Slide 3: What’s my problem?
The weakest link in Cyber Security as a whole..

## Slide 4
Human Error

## Slide 5: Today’s Topics
The Problem at Hand
Researching the Problem
Project Overview
  Hardware/Software
  Process
Application of Project/Outlook

## Slide 6: Back to the problem
Human error in the general public is imminent with cyber security.
Social Engineering’s high success rate with people in general.
People are simply just uneducated about cyber security.

## Slide 7: What makes this dangerous?
The everyday person is aware of hackers and scams.
Need to understand these scams and phishing schemes on a more technical level.
In both the private & government sectors, everyday people are the exploit that hackers prefer.

## Slide 8: Examples
Syrian Electronic Army’s attack on the Associated Press’ Twitter.
  Simple email spear-phishing attack.
  Human Error could be avoided within victim.
Teenager’s simple attack gaining access to CIA director’s email.
  Simple phone call social engineering.
  Human Error could be avoided within resources surrounding victim.

## Slide 9: Cyber Maryland Conference 2015
I attended the 2015 Cyber Maryland Conference in Baltimore, MD
  Educational Workshops
  Lots of Private/Government Sector Companies
One particular presentation caught my attention and was very interesting, as I was working on this project.
Albert Schultz, CEO of Krypteia , LLC presented on “The Human Element”

## Slide 10: Project overview
Wanted to create something that exemplified my skillset, as well as something that would serve as an example for solving the problem researched.
The idea came out of my passion for working with Raspberry Pi’s, Servers, & Designing Websites.
Resulted in: Portable User Interface for Cyber Security Awareness

## Slide 11: Computing hardware
Assorted USB Cables
USB WiFi Dongle
10,000 mAh Lithium Ion Battery
Raspberry Pi 2 Model B
  A 900MHz quad-core ARM Cortex-A7 CPU
  1GB RAM
  8GB MiniSD Card Storage
Raspberry Pi 7” Touchscreen Display
  4 Standoff Screws/Bolts
  4 GPIO Jumper Wires
  Ribbon Cable
  Display Adapter Board

## Slide 12: Software
Raspbian Wheezy Operating System (Debian Based)
Chromium Browser
Unclutter
lighttpd Local Server
fbi Startup Screen
Manipulation of LXDE Startup Script

## Slide 13: Casing Hardware
4 Sq. Ft. White Composite Board
Trim Head Stainless Steel Screws
Oak Wood Piece
Light Gauge Steel Strapping
¾ In. Black Screws (Wide Heads)

## Slide 14: Hardware Tools
Small Screwdriver
Cordless Electric Drill
Square
Table Saw
Electric Router
Compound Mitre Saw
Jigsaw
Lineman Pliers
Material Clamps

## Slide 15: Software Tools
WinSCP
Apache Web Server
SD Formatter
Win32DiskImager
Adobe Dreamweaver CC 2015
Adobe Illustrator CC 2015

## Slide 16: Process
Assembled Computer Hardware:
  Attached Display Adapter Board to Touchscreen
  Attached Raspberry Pi 2 to Display Adapter Board with Standoffs
  Connected Ribbon Cable from Raspberry Pi 2 to Adapter Board
  Connected Jumpers from adapter board to appropriate GPIO pins on the Raspberry Pi 2
-- 5V
-- GND
-- SDA
-- SCL

## Slide 17: Process (Cont.)
Began Computer Function:
  Installed Raspbian Wheezy Operating System onto MicroSD Card using Win32DiskImager
  Booted up the Raspberry Pi and configured the OS (raspi-config)
  Inserted USB WiFi Dongle and configured network settings
  “sudo apt-get update && sudo apt-get upgrade”

## Slide 18: Process (Cont.)
Configured Kiosk Function:
  “sudo apt-get install chromium unclutter”
  Configured LXDE Startup File: “sudo nano /etc/xdg/lxsession/LXDE-pi/autostart” with
  “@chromium --kiosk http://www.nicjones.org/stsp.html --incognito” as the last line
  Disabled Auto-Sleep “sudo nano /etc/lightdm/lightdm.conf” with
  “xserver-command=X -s 0 dpms” under the “[Seat Defaults]” Section
  Configured Boot Image: “sudo apt-get install fbi” and put
      My custom “Splash.png” made in Illustrator in “/etc/”

## Slide 19: Process (Cont.)
Website Design:
  Troubleshot Screen Resolution, Zoom, & Size for Chromium
  Created logo, and banner buttons in Adobe Illustrator
    Including: Home, Research, Phishing, Exploits, AntiVirus, News, & Utilities
  Fabricated the Website Template in Adobe Dreamweaver

## Slide 20: Process (Cont.)
Testing the Website on the Webserver:
  Another Raspberry Pi Model B Running Apache Web Server at home
  Has SSH Enabled
  Using WinSCP on my Windows PC I connected via SFTP to my other Raspberry Pi
  Sychronized website directory on my Windows PC to Raspberry Pi “/www/” directory
  Already had a webserver running before so port-forwarding to the domain with GoDaddy.com was already set up

## Slide 21: Process (cont.)
Website Design (cont.):
  Template complete with all banner links and rollover buttons working
  Time to create the web pages and fill them in with content
  RSS feed script was used
  Some pages use the “<iframe>” HTML tag to contain other websites within my own
    Used the “sandbox” attribute with “<iframe>” so that the user could not go to an external site

## Slide 22: Process (cont.)
Website Design (cont.):
  The Home page
  The Research page
  The Phishing page
  The Exploits page
  The AntiVirus page
  The News page
  The Utilities page

## Slide 23: Process (cont.)
Website Completion:
  At this point the website was complete
  All hyperlinks working as they need to
  But WHAT would I do if there was no WiFi?
    I created a separate special Offline version of the Website
    Hosted it on a local server on the device using lighttpd
    Created a button under the “Utilities” tab to resort to the offline version
    Configured the Raspberry Pi to boot up into the offline version first

## Slide 24: Process (cont.)
Now for the Casing:
  Decided on using Composite Board as the main material
  First measured and cut the face frame for the screen
  Routed the edges of the frame to give it a cleaner look

## Slide 25: Process (Cont.)
Mounting the Screen to the Frame:
  Used a jigsaw to cut out the inside square of the frame
  Wanted a discrete and non-damaging mount to the screen
  Used a strong piece of Oak wood to pinch the very edges of the screen to the frame
  Used wide headed screws to fasten the Oak to the frame, securing the screen
  Cut the tips of the screws using Lineman’s Pliers so they did not stick through the front

## Slide 26: Process (Cont.)
Creating the Structure:
  Time to create the main body of the casing
  Cut the measured pieces of composite using the Compound Mitre Saw & Table Saw
  Created a shelf for the battery on the inside without interfering with the Raspberry Pi
  Secured composite pieces with Trim Head Stainless Steel Screws

## Slide 27: Process (cont.)
Finished off the Casing:
  Slotted the edges of the casing with the table saw to have a sliding back to close
  Attached the frame and hardware to the casing with precision using Trim Head Stainless Steel Screws
  Cut out a tightly fitting piece of composite to slide in and close the back
  Created a routed hole in the sliding piece for ease of access

## Slide 28: Process (cont.)
Connecting Battery and Power:
  Secured the battery to the case with an angled piece of Light Gauge Steel Strapping
  Used an angled USB Type A Female connector to connect power to the Raspberry Pi via a USB Micro type with a USB from the 2A supply port on the battery
  Included a USB Type A switch in series for easier on/off function
  Have a female USB type B Micro for charging the battery inside

## Slide 29: The final Product
The final product is overall very clean and functional
Best feeling to start it up in the finished case
Tested it within range of WiFi and within range of WiFi
Although it isn’t perfect, it is unique and something that I built

## Slide 30: What changed?
What changed along the way that was not part of my original planning?
  Originally considered Plexiglass for the casing but instead used Composite
  Wanted to have an outer installed power switch but put it on the inside
  Intended on it being thinner

## Slide 31: What Changed? (cont.)

## Slide 32: Problems
What problems did I have along the way?
  Took a long time to get the screen resolution of the website to perfectly fit the screen
  Had to reinstall the operating system and resources MULTIPLE times

## Slide 33: What did I learn?
Troubleshooting and Testing of Websites
Considering the User
Planning ahead

## Slide 34: Back to the problem
The people involved in using systems for what they’re made to do, need to be more educated on how to protect themselves on them
They need a general platform for understanding how to protect themselves on the most basic level needed against cyber attacks
If the weakest link can be fixed, cyber security can be greatly improved

## Slide 35: Where My project comes in
My hope is not that my project is what people use in order to be more educated about cyber security
My project is just a start
My project can serve as an example to start an initiative for more professional cyber education platforms to be developed

## Slide 36
Thank You
Any Questions?